## Slide 1: Technical Arts (TA 101AA) Engineering Graphics
Prof. Nachiketa Tiwari
Department of Design

## Slide 2
Solid-Solid Interactions

## Slide 3: Intersection of a Plane & a Cone
Method 1: Selected Line Method - When an edge view (EV) of the plane is available!
1
2
3
4
5
6
7
8
9
10
11
12
v
v
1
2
3
4
5
6
7
8
9
10
11
12
a
b
c
l
k
d
j
e
i
f
h
g
In FP, the cone is seen as a triangle and the plane as Edge View.
Draw lines V-1, V-2 , etc. called ‘elements’ or ‘generators’ in top and front views.
The points of intersection of ‘generators’ and EV give the ‘line of intersection’ of plane and cone in FP.
Locate the points of intersection (e and i) in the HP.
Similarly, locate all other points of intersection in top view and draw the ‘curve of intersection.’
What will be the shape of the ‘curve of intersection’ in top view?
Plane in EV
i
e
a
b
c
d
f
g
h
j
k
l
HP
FP

## Slide 4: Intersection of a Plane & a Cone
Method 2: Cutting Plane Method -When an oblique plane cuts the cone
Cutting plane
1
2
3
5
6
7
8
9
10
11
12
Draw generators in both top and front views.
Pass a ‘vertical cutting plane’ through generators
V-2 and V-8, it will be in EV in top view.
The ‘cutting plane’ cuts the cone in two halves; and cuts the oblique plane at points X and Z.
Transfer the points X-Z in the VP.
Points of intersection of line X-Z with generators
(V-2 and V-8) in VP yield desired ‘points of intersection of cone and the oblique plane’.
Transfer these ‘points of intersection’ (b and h) from VP to HP.
Similarly, get all other points of intersection.
v
a
b
c
d
e
f
g
i
j
k
l
XH
ZH
v
1
2
3
4
5
6
7
8
9
10
11
12
a
c
d
e
f
g
h
i
j
k
l
XF
ZF
4
HP
VP
b
h

## Slide 5: Importance of Solid-Solid Intersections?

## Slide 6: Intersection of Two Solids
Two Methods:
  Selected line method
    Select sufficient number of lines on a surface.
    Find the points where each of these lines pierces the other surface.
    A line joining these piercing points would give the curve of intersection between the two surfaces.

## Slide 7: Intersection of Two Solids
Two Methods:
  Cutting plane method
    Pass a number of cutting planes through each of the given surfaces simultaneously.
    Each plane will cut a line (straight or curved) from each given surface.
    These lines will intersect in a point (or points) common to both surfaces.
    A curve connecting those points will give the curve of intersection between the two surfaces.

## Slide 8: Two Prisms: Selected Line Method
(q’H), s’H
r’H
p’H
aH, (a’H)
bH, (b’H)
dH, (d’H)
a’V,(c’V)
b’V
d’V
1
2
3
5
6
7
1H,(3H)
2H
4
5H, (7H)
6H
8
1V
2V
3V
(4V)
5V
7V
6V
(8V)
a
b
c
d
a’
b’
d’
aV,(cV)
bV
dV
(qH), sH
rH
pH
(pV), rV
qV
sV
(p’V), r’V
q’V
s’V
p
q
s
r
q’
s’
r’
cH, (c’ H)
Project 4-2 and 8-6 from HP and find the intersection with p-p’ in VP
Join the intersection lines 1-2, 3-2, 5-6 and 7-6
HP
VP

## Slide 9
1H
2H
3H
4H
7H
10H
6H
5H
11H
12H
8H
9H
1F
3F
4F
5F
2F
6F
7F
12F
11F
10F
9F
HP
VP
P
5P,3P
6P,2P
7P,1P
10P
8P,12P
Two Cylinders: Selected Line Method
9P,11P
4P
8F

## Slide 10: Intersection of Two Cylinders
1H
2H
3H
4H
7H
10H
6H
5H
11H
12H
8H
9H
1F
3F
4F
5F
2F
6F
7F
12F
11F
10F
9F
H
F
P
5P,3P
6P,2P
7P,1P
10P
8P,12P
1
12
11
10
9
8
7

## Slide 11
1
2
3
4
4’
3’
2’
2
1
3
4
A
B
C
D
D
C
B
A
4
3
2
1’
4’
3’
2’
Two Cylinders: Cutting Plane Method
Draw the principal views.
Take a ‘vertical cutting
plane’ cutting one
of the cylinders (vertical one)
in front view.
Draw the ‘cutting plane’ in profile view and get its intersection with the other (horizontal) cylinder.
The points of intersection of two cylinders are located in front view through projectors from top and profile views.
Repeat this process by taking more ‘cutting planes’ and get the corresponding ‘points of intersections’ in VP.
Join the points 4’-3’-2’-1-2-3-4 to get the ‘curve of intersection’.
HP
VP

## Slide 12: Two Cylinders

## Slide 14: Cylinder & Prism: Selected Line Method
Note that the backside of the intersection overlaps with the front side.

## Slide 15: Cylinder & Prism: Selected Line Method
Note that the backside of the intersection overlaps with the front side.

## Slide 16: Cylinder & Cone: Selected Line Method

## Slide 17: Intersection of Cone and Cylinder

## Slide 18: Intersection of Cone and Cylinder

## Slide 19: Cone-Cylinder: Selected Line Method
g
j
d
c
k
a
b
c
d
e
g
i
j
k
l
a
b, l
c, k
d, j
e, i
g
a
1
2
3
4
5
6
7
8
9
10
11
12
4
3, 5
2, 6
1, 7
8, 12
9, 11
10
7
6, 8
5, 9
4, 10
3, 11
2, 12
1
a
b
b
l
l
c
k
j
d
i
e
i
e
g
O
O
O
HP
VP

## Slide 20: Thank You