## Slide 1: Technical Arts (TA 101AA) Engineering Graphics
Prof. Nachiketa Tiwari
Department of Design

## Slide 2
Orthographic Projections

## Slide 3: Why Engineering Drawings?
How would you describe this object to others?
  Shape.
  Size and dimensions
  Surface finish
  Material
  Tolerances
Engineering graphics: To provide unambiguous understanding to all.
  A fundamental means of communication: manual or thru computer.

## Slide 4: ENGINEERS USE 2D IMAGES BASeD ON ORthOGRAPHIC PROJECTIONS

## Slide 5: Type of Projections
Center of Projection at Infinity
Center of Projection
Picture Plane
Picture Plane
Perspective or Converging
Parallel

## Slide 6: Type of Projections
Lines from coordinate in Original Space to coordinate in Projected Space

## Slide 7: Orthographic Projection
A special type of parallel projection.
Projector lines are not only mutually parallel, but also perpendicular to the plane of projection.
Real world objects are mapped onto a 2D drawing sheet.

## Slide 8: The Six Principal Views
The 6 principal views can be created by looking at the object from different directions.
However, for most objects, three orthographic views are adequate to represent a 3D object.

## Slide 9: Orthographic Views Third Angle Convention
Imagine the object of study is placed inside a glass box.
The sides of the box represent the 6 planes of projection.
Planes are mutually connected by hinge joints.
Frontal Plane
Horizontal Pane
Profile Plane

## Slide 10: Orthographic Views Third Angle Convention
The image of the object is projected on each of the six sides of the box.

## Slide 11: Orthographic Views Third Angle Convention
Next, the box is unfolded creating the 6 principal views as shown below.

## Slide 12
Label the 5 remaining principal views with the appropriate view name.

## Slide 13
Name each view.
Top

## Slide 14
Name each view.
Top
Right Side

## Slide 15
Name each view.
Top
Rear
Right Side

## Slide 16
Name each view.
Top
Rear
Left Side
Right Side

## Slide 17
Name each view.
Top
Rear
Left Side
Bottom
Right Side

## Slide 18
What are the differences between the Right Side and Left Side views?
Top
Right Side
Rear
Left Side
Bottom
They are mirror images with one different line type.

## Slide 19
What are the differences between the Top and Bottom, and Front and Rear views?
Top
Right Side
Rear
Left Side
Bottom
They are mirror images with different line types.

## Slide 20
Top
Right Side
Rear
Left Side
Bottom

## Slide 21: Selecting the Right “Front” View
The front view should show maximum number of features of the object.
  Should have least amount of hidden lines.
  The front view is chosen first and the other views are based on the orientation of the front view.

## Slide 22
The top and front views are aligned vertically and share the same width dimension.
Alignment of Different Views
The front and right side views are aligned horizontally and share the same height dimension.

## Slide 23: Orthographic Projections Third Angle Convention
Object in 3rd quadrant.
Plane of projection is transparent.
Observer -> Plane of projection -> Object.

## Slide 24: Orthographic Projections Two Conventions
THIRD ANGLE
Object in 3rd quadrant.
Plane of projection is transparent.
Observer -> Plane of projection -> Object.
Front view below horizontal axis.
FIRST ANGLE
Object in 1st quadrant.
Plane of projection is opaque.
Observer -> Object -> Plane of projection.
Front view is above horizontal axis.
Context: Developing the Front View

## Slide 25: First Angle Convention

## Slide 26: First Angle Convention
Object in 1st quadrant.
Plane of projection is opaque.
Observer -> Object -> Plane of projection.
Front view is above horizontal axis.
Top view below the front view and vice-versa.
Right side view is left of front view, and vice-versa.
Used in India, UK, and parts of Europe. However, BIS is OK with either standard.
Symbolized as

## Slide 27: Third Angle Convention

## Slide 28: Third Angle Convention
Object in 3rd quadrant.
Plane of projection is transparent.
Observer -> Plane of projection -> Object.
Front view is below horizontal axis.
Top view is above the front view and vice-versa.
Right side view is right of front view, and vice-versa.
Used in USA.
Symbolized as

## Slide 29: Line Types
Visible lines
  Visible lines represent visible edges and boundaries.
  Continuous (0.5 - 0.7 mm).
Hidden lines
  Hidden lines represent edges and boundaries that cannot be seen.
  Dashed .
Center lines
  Represent axes of symmetry.
  Long dash – short dash .

## Slide 30: Edges
Represent locations where planes/surfaces meet transversally or material boundaries exist!

## Slide 31: Tangent arcs or tangent lines No edges at tangent points! Smooth transition
Front view without internal details
Would there be lines corresponding to the tangent points?

## Slide 32: Creating Hidden Lines
Hidden lines represent invisible edges and boundaries.
The length of hidden line dashes may vary slightly as the size of the drawing changes.

## Slide 33: Using Center Lines
Center lines indicate axes of symmetry.
  They are important for interpreting cylindrical shapes.

## Slide 34: Drawing Center Lines
Extend a little beyond the object or feature.
Start and end with long dashes.

## Slide 35: Drawing Center Lines
May be connected within a single view to indicate that two or more features are coplanar.
  Should not extend in the space between views .

## Slide 36
Hinge/ Folding Lines


Dashes of uniform lengths and spacing

## Slide 37: Precedence of Lines
What happens when multiple lines are coincident ?
Priority
  Object Line
  Hidden Line
  Cutting plane/ section line
  Center Line

## Slide 38
Example

## Slide 39: Creating Orthographic Projections
Choose the front view appropriately.
  Which view shows the most about the object?

## Slide 40: Creating Orthographic Projections
How many views are really needed to describe the object completely?
  Which are those views?
Just for explanation purpose, we will draw all 3 standard views.

## Slide 41: Creating Orthographic Projections
Draw the four quadrants
Draw visible features of the front view.
Folding line

## Slide 42: Creating Orthographic Projections
Draw projectors from the front view.
  2H pencil
  Continuous lines.

## Slide 43: Creating Orthographic Projections
Draw the top view.

## Slide 44: Creating Orthographic Projections
Project back to the front view, if required.

## Slide 45: Creating Orthographic Projections
Draw a 45 miter line.
  Continuous
  2H pencil
Miter
line

## Slide 46: Creating Orthographic Projections
Draw projectors over to the 45 miter line and down to form object feature points.

## Slide 47: Creating Orthographic Projections
Draw the right side view.
Project back if needed.
Draw centerlines if needed.

## Slide 48: Let us Review What We Drew.

## Slide 49: The Final Drawing Third Angle Projection

## Slide 50
Exercise

## Slide 51
Fill in the visible lines in the top view.

## Slide 53
Fill in the visible lines in the front view.

## Slide 55
Fill in the visible lines in the right side view.

## Slide 57
Fill in the hidden lines in all the three views.

## Slide 59
Draw the center lines in all views.

## Slide 61: In this course, your should …
leave the construction lines after completing your drawing.
use a 45o miter line for reflecting the views.
use 2H pencil for all construction lines.
use H pencil for object lines, dimensions, writing, etc.

## Slide 62
Some objects can be described by just one view.

## Slide 63: Flat Parts of Uniform Thickness
No extra information provided by these two view.
Not needed.

## Slide 64: Objects with Circular Cross-sections
Similarly, objects with square cross-sections need only one view.

## Slide 65
Some objects can be described by only two views.

## Slide 67: Practice Problems